Corporate Communications Hans-Robert Koch Phone: +49 2772 505-2693 Fax +49 2772 505-2537 E-mail: koch.hr@rittal.de Christian Abels Phone: +49 2772 505-1328 Fax: +49 2772 505-2537 E-mail: abels.c@rittal.de Rittal GmbH & Co. KG Auf dem Stützelberg 35745 Herborn, Germany www.rittal.com

Rittal cable clamp rail for EMC shielding bracket with strain relief

Installing cables easily

If cables can be easily installed in the enclosure in an EMC-compatible way, and if strain relief can be provided at the same time, this will save an enormous amount of time during electrical installation work. This is particularly true if it can be achieved with a single component such as the Rittal cable clamp rail for EMC shielding bracket with strain relief. It helps to reduce the complexity of the electrical interior design of enclosures.

Herborn, 23 August 2016 – Fitting cables with different diameters in enclosures and installing them safely are complex matters and often very time-consuming. There are two imperatives: effective strain relief on the one hand, which protects a cable connection to a connection point from mechanical burdens, and very often electromagnetic compatibility (EMC) on the other hand. EMC-compatibility in this respect means that shielded cables must form a contact to the enclosure and to the mounting plate close to their point of entry. Because of this contact, interference currents that result from fast-switching processes in devices (such as frequency converters) are then diverted to their very source in the system by using a potential equalisation.

All these requirements can now be implemented easily and quickly with the Rittal cable clamp rails for EMC shielding brackets with strain relief, starting from the embedded C-section structure that allows flexible positioning of the cable clamps and therefore high packing densities, through the flexible and easy attachment of the EMC shielding bracket, to the simple cable attachment to T-heads with cable ties. The mounting brackets (among the goods supplied) ensure flexible positioning and a conductive connection on the enclosure section or mounting plate.

(1,785 characters)



Caption(s)

fri131317500.jpg: The Rittal cable clamp rail for EMC shielding bracket with strain relief helps reduce the complexity of the electrical interior construction of enclosures significantly.

May be reproduced free of charge. Please name Rittal GmbH & Co. KG as the source.

About Rittal

Rittal, headquartered in Herborn, Germany, is a leading global provider of solutions for industrial enclosures, power distribution, climate control and IT infrastructure, as well as software and services. Systems made by Rittal are deployed across a variety of industrial and IT applications, including vertical sectors such as the transport industry, power generation, mechanical and plant engineering, IT and telecommunications. Rittal is active worldwide with 10,000 employees and 58 subsidiaries.

Its broad product range includes infrastructure solutions for modular and energy-efficient data centres with innovative concepts for the security of physical data and systems. Leading software providers Eplan and Cideon complement the value chain, providing interdisciplinary engineering solutions, while Rittal Automation Systems offer automation systems for switchgear construction.

Founded in Herborn in 1961 and still run by its owner, Rittal is the largest company in the Friedhelm Loh Group. The Friedhelm Loh Group operates worldwide with 18 production sites and 78 international subsidiaries. The entire group employs more than 11,500 people and generated revenues of around €2.2 billion in 2014. In 2015, it was named one of Germany’s leading employers by the Top Employers Institute, for the seventh year running.

For more information, visit www.rittal.com and www.friedhelm-loh-group.com.