Corporate Communications Regina Wiechens-Schwake Phone: +49 2772 505-2527 E-mail: wiechens-schwake.r@rittal.de Hans-Robert Koch Phone: +49 2772 505-2693 E-mail: koch.hr@rittal.de Christian Abels Phone: +49 2772 505-1328 E-mail: abels.c@rittal.de Rittal GmbH & Co. KG Auf dem Stützelberg 35745 Herborn, Germany www.rittal.com

Rittal expands RiLine Compact portfolio

Shock-hazard protected, compact and simple: Rittal expands its board systems

Rittal is adding new components to its successfully launched RiLine Compact busbar system for small control systems and switchgear. The components are for example a larger infeed up to 125 A,  a single-pole component adaptors for 18-mm wide circuit-breakers and new slim motor controllers. The system, which permits the easy installation of distributions for currents of up to 125 A, can now be used universally.

Herborn, 15 February 2019 – Following the successful launch of its new “RiLine Compact” busbar system at the start of the year 2017, Rittal is now further expanding its RiLine Compact range to include a variety of new components. These components, when used in control and switchgear with a maximum current of up to 125 A and with completely shock-hazard protected boards make installation easier and shorten the time needed for installation. The components are simply plugged onto the board and so acquire both their mechanical and electrical connections in a single assembly operation.

Connecting boards with an adaptor extension

The new infeed adaptor for currents up to 125 A features parallel mechanical and electrical contacts. This way, two RiLine Compact Boards can be easily and securely connected to form a larger system. The adaptor has a build width of 45 mm and is suitable for connecting cables with cross-sections of up to 50 mm².

Further innovations are the single-pole, 18-mm wide component adaptors. The narrow adapters for accommodating power circuit-breakers are available in two versions for 16 A and 63 A. There are three different versions of each, for connection to L1, L2 or L3. An adapter (also 18-mm wide) without any electrical connection to the busbar system can be used as equipment support for a variety of components.

Half as much space is needed

The range of motor controllers is also being expanded. These are now available ex-stock for the 0.6, 2.4 and 9 A current ranges. They combine the direct starter and reversing starter functions in one device and are only 22.5 mm wide. That means freeing up around 50 per cent more space compared to the standard 45 mm for sealing switching device in this current range and as much as 75 per cent more space compared to the 90 mm-wide reversing combinations. The three-phase motor controllers are high-performance hybrid switching devices that include a current monitoring function. With its hybrid technology, the device offers a longer lifespan and low-loss operation. The principle behind it is simple: First, the electronics are switched on via the input signal, and then the mechanical contacts take over for the main duration. The motor controller offers even more advantages with its diagnostic function, which it uses to detect internal and external errors.

Compact distributions are now easy to set up

With the RiLine Compact busbar system, distributions with a rated current of up to 125 A can be achieved in a very space-saving manner. Because the components are simply plugged onto the board, the work involved in installation is very small. The time and effort spent on wiring is greatly minimised thanks to the motor controllers with their internal circuitry and wiring. RiLine Compact is suitable for applications where many protective devices have to be accommodated in confined spaces within the enclosure. The small busbar system for up to 125 A can be used, for example, for controlling the flaps in ventilation systems, cooling systems and much more.

(3,581 characters)



Caption

fri172037000.jpg: With new motor controllers for its RiLine Compact system, Rittal offers an elegant, slimline solution.

May be reproduced free of charge. Please name Rittal GmbH & Co. KG as the source.

About Rittal

Rittal, headquartered in Herborn, Hessen, Germany, is a leading global provider of solutions for industrial enclosures, power distribution, climate control and IT infrastructure, as well as software and services. Systems made by Rittal are deployed across a variety of industrial and IT applications, including vertical sectors such as the transport industry, power generation, mechanical and plant engineering, IT and telecommunications. Rittal is active worldwide with 9,300 employees and 58 subsidiaries.

Its broad product range includes infrastructure solutions for modular and energy-efficient data centres with innovative concepts for the security of physical data and systems. Leading software providers Eplan and Cideon complement the value chain, providing interdisciplinary engineering solutions, while Rittal Automation Systems offers automation systems for switchgear construction.

Founded in Herborn in 1961 and still run by its owner, Rittal is the largest company in the Friedhelm Loh Group. The Friedhelm Loh Group operates worldwide with 18 production sites and 80 international subsidiaries. The entire group employs 11,500 people and generated revenues of €2.5 billion in 2017. For the tenth time in succession, the family business has won the accolade “Top German Employer” in 2018. In addition Friedhelm Loh Group was recognized as “Top vocational trainer” according to a study of Deutschland Test and Focus Money for the third year running in 2018.

Further information can be found at www.rittal.com and www.friedhelm-loh-group.com.