New cooling container for standardised data centre

A cool addition

Rittal has added a fully pre-configured cooling container to RiMatrix S, its modular, standardised data centre. This cooling solution works primarily with indirect free cooling, and as a result, it is extremely energy-efficient – with a power usage effectiveness (PUE) of up to 1.15. It can be installed in less than a day – much faster than a conventional climate control solution.

Herborn, Germany, 3 September 2014 – The cooling container, available now, consists of a high cube-type container frame (6.06 m length x 2.44 m width x 2.89 m height). A hydraulic enclosure, two cooling units and a free cooler are mounted onto the frame, while two cooling pipes and a power supply connect the climate control solution to the RiMatrix S data centre. As the container works primarily with indirect free cooling, there is no need to use an energy-intensive chiller (compressor) when the outside temperature is sufficiently low. Speed-controlled EC (electronically commutated) fans, redundant pumps, and a controller than automatically adapts output to the RiMatrix S server module’s cooling needs, ensure very high energy efficiency – with a PUE of up to 1.15 in operation.

Three operating modes

The heat exchanger for indirect free cooling is filled with a water/glycol mixture and is capable of dissipating a heat output of 70 kW for the Single 6 version of RiMatrixS, or 100 kW for the Single 9 version. The two chillers are hooked up if outside temperatures rise – each of these redundant devices is rated 70 or 100 kW, respectively, ensuring a highly available cooling output. Three operating modes are possible, depending on the outside temperature: indirect free cooling alone, a hybrid mode using both free coolers and chillers, and chillers alone. Either the free coolers or the chillers, or both, use the redundant central pumping unit, depending on the operating mode.

Integrated monitoring and control

The cooling container is mass-produced. Its smart controller ensures that the generated cooling output adapts to the changing requirements of the RiMatrix S server module. A network interface transmits recorded temperature data via SNMP (Simple Network Management Protocol) to Rittal’s RiZone management software, or to another DCIM (Data Centre Infrastructure Management) platform. In addition, this interface creates a link to a web server, where the user can adjust the cooling solution’s parameters and monitor its current status. In the event of a fault, floating signal contacts alert the administrator – enabling a rapid response.

(2.604 characters)



Bildmaterial:

fri141770100.jpg: Rittal’s new cooling container is the latest addition to RiMatrix, its modular, standardised data-centre system. The solution works primarily with indirect free cooling, making it extremely energy-efficient, with a PUE of up to 1.15.

May be reproduced free of charge. Please name Rittal GmbH & Co. KG as the source, and provide us with a sample copy.

Rittal GmbH & Co. KG

Rittal GmbH & Co. KG, headquartered in Herborn, Germany, is a leading global provider of solutions for industrial enclosures, power distribution, climate control and IT infrastructure, plus software and services. Systems made by Rittal are deployed in a variety of industries, including mechanical and plant engineering, IT and telecommunications.

The company’s broad portfolio includes complete solutions for modular and energy-efficient data centres: from innovative security concepts for data systems to physical data and system security for IT infrastructures. Thanks to leading software vendor Eplan’s interdisciplinary engineering solutions, and Kiesling Maschinentechnik’s automation concepts for switchgear manufacture, Rittal covers most aspects of the value chain.

Founded in 1961, Rittal is now active worldwide with 11 production sites, 64 subsidiaries and 40 agencies. With 10,000 employees worldwide, Rittal is the largest company in the owner-operated Friedhelm Loh Group, based in Haiger, Germany. The entire group employs more than 11,500 people and generated revenues of around €2.2 billion in 2013. Further information at www.rittal.com and www.friedhelm-loh-group.com.

# Text boxes

Corporate Communications Kerstin Ginsberg Tel.: +49 2772/505-1328 Fax: +49 2772/505-2537 E-Mail: ginsberg.k@rittal.de Patricia Späth Tel.: +49 2772/505-2346 Fax: +49 2772/505-2537 E-Mail: spaeth.p@rittal.de Rittal GmbH & Co. KG Auf dem Stützelberg 35745 Herborn www.rittal.com