Media Relations Contact Richard Andrews Marketing Services Manager Tel: 01709 704000 e-mail: information@rittal.co.uk Rittal Limited Braithwell Way Hellaby Industrial Estate Hellaby Rotherham S66 8QY www.rittal.co.uk

Date of issue: February 20, 2017

Busbar Systems and IEC 61439 Standards

Busbars systems, or busbar supports are essentially heavy conductors, typically made of copper, which carry and distribute powerful electric currents to components that consume electrical power throughout an assembly.

Busbars are not only easy to install (certainly compared to cabling), they also play a major role in the design and safe operation of a switchgear and controlgear assembly.

The recent introduction of the IEC 61439 switchgear and control standards has significant implications for the design and performance of the copper busbar system.  It’s an area which engineers need to appreciate, not least because the new testing regime and the requirement for compliance has changed the way we think about the selection of the busbar system.

One of the most important requirements of any switchgear power

distribution system is to carry fault currents (short circuits) safely

until a protection device, namely the fuse or the moulded case

circuit breaker, interrupts the fault.

This capability, and the product specification, is the subject of

testing which is covered by the IEC 61439 standard and which

provides vital information for building a safe assembly.

Busbar testing, in fact, was revolutionised following the

introduction of the standard which came into force in

November 2014.  It continued a determination across the

sector to harmonise the low voltage industry through the creation

of one standard which provided protection for both personnel

and switchgear.

IEC 61439 requires busbar systems to be tested – by their

manufacturers - within enclosures rather than (as previously

happened) as a standalone arrangement.  This is a step forward

for the industry, providing access for system engineers to data

delivered in situ which offered both a more realistic assessment

and more accurate and reliable data than before.

Further information at www.rittal.co.uk and

www.friedhelm-loh-group.com or on twitter @rittal_ltd.

Ends

Press Information:
Richard Andrews,
Marketing Services Manager,
Email: information@rittal.co.uk

Image

Picture shows: Rittal Low Voltage Directive Guide
Reproduction free of charge
Please specify “Rittal Limited” as source
Please send us a reference copy

Notes to Editors

Rittal, headquartered in Herborn, Hessen, Germany, is a leading global provider of solutions for industrial enclosures, power distribution, climate control and IT infrastructure, as well as software and services. Systems made by Rittal are deployed across a variety of industrial and IT applications, including vertical sectors such as the transport industry, power generation, mechanical and plant engineering, IT and telecommunications. Rittal is active worldwide with 10,000 employees and 58 subsidiaries.

Its broad product range includes infrastructure solutions for modular and energy-efficient data centres with innovative concepts for the security of physical data and systems. Leading software providers Eplan and Cideon complement the value chain, providing interdisciplinary engineering solutions, while Rittal Automation Systems offers automation systems for switchgear construction.

Founded in Herborn in 1961 and still run by its owner, Rittal is the largest company in the Friedhelm Loh Group. The Friedhelm Loh Group operates worldwide with 18 production sites and 78 international subsidiaries. The entire group employs more than 11,500 people and generated revenues of around €2.2 billion in 2014. For the seventh time in succession, the family business has won the accolade “Top German Employer” in 2015.

Further information can be found at www.rittal.com and www.friedhelm-loh-group.com.